Q THEATRE

Technical Specifications

27/02/08

Technical Manager:

Phone number:02 47237608

Mobile Number:0414 983316

Fax number:     02 47313701

Email address: technical@jspac.com.au

Venue:

Phone number:02 47237611

Fax number:    02 47313701

Website:	www.jspac.com.au

STAGE

Brief Stage Description:

Unraked stage with sort of Pros Arch. Plywood floor. Screwing or nailing into surface is permitted. Stage crossover is best via corridor backstage but is possible behind Cyc

Stage distributed load limit   Not Determined

Stage point load limit	Not Determined

.

Stage rake	No

Stage Dimensions:

Proscenium	It is a pretend Proscenium.

Width                  14 mtrs actual 12 mtrs practical

Height	6500 underside catwalk

6350 to obstruction

Setting Line

Setting line is determined by stage elements & sight lines.

It is more appropriate to take measurements from Proscenium Line

Distance From (PL = Proscenium Line, CL = Centre Line)

PL to DS edge of apron	5 Mtrs

PL to first fly line	1.8 Mtrs

PL to last upstage fly line	6 Mtrs

PL to rear wall 	8 Mtrs

CL to OP wall (or obstruction)	13.2 Mtrs

CL to PS wall (or obstruction)	8.3 Mtrs

Stage to underside of grid	6350

.

Overhead obstructions

Catwalk

.Auditorium:

Raked seating. Plan available on website

Seating capacity                                    375

Flying Facilities:

Fly System

Hand winch

.

Fly System Details

Operating Position	Prompt Side in Catwalk

Total number of Lines	8

Batten Drift	8 Mtrs

.

Batten Type 	48 mm O/D Pipe

Batten Length	14 Mtrs

Batten Pick-ups	6

Batten Point Load	Not determined

Batten W.L.L.	350 Kgs

”

LX bars can be swung	A little bit

SEE HANGING PLOT FOR LINE ALLOCATIONS AND FURTHER INFO

Hanging Plot:

### PL: Pros as indicated previously

Line Type: SP = Single purchase,  DP = Double purchase,  MW = Motor Winch,  HW = Hand Winch,  HL = Handline

W.L.L.: Maximum distributed load including bar weight

| Line # | Distance from PL | Line Type | W.L.L | Venue Allocation | Intended Use (hiring company use) |
| --- | --- | --- | --- | --- | --- |
| 1 | 1800 | HW | 350kg | LX 1 HW | Venue allocation |
| 2 | 2400 | HW | 350kg | LX 2 HW | Can be changed to |
| 3 | 3000 | HW | 350kg | Border HW | Suit hirer |
| 4 | 3600 | HW | 350kg | LX 3 HW |  |
| 5 | 4200 | HW | 350kg | LX 4 HW |  |
| 6 | 4800 | HW | 350kg | Cyc units HW |  |
| 7 | 5400 | HW | 350kg | Tab HW |  |
| 8 | 6000 | HW | 350kg | Cyclorama HW |  |

Drapery:

| *Type | Material | Colour | Width | Height | Quantity |
| --- | --- | --- | --- | --- | --- |
| Cyclorama |  | White | 14000mm | 6800mm | 1 |
| Borders | Wool 50% gathered | Black | 14000mm | 2400 | 3 |
| Legs/Book Flats | Timber frame Felt | Black | 1200mm/”page” | 5000mm | 6 |
| Tabs / | Wool 50% gathered | Black | 14000mm | 6800mm | 1 pair |

Access Equipment:

Elevated Work Platform

Instant Zip Up

Maximum reach is 24 Ft

EWP Restrictions

Outriggers must be used at all times, only to be used by trained competent persons

.

Ladders

(1) 5ft A frame

(2) 8ft A frame

(1) 12ft A frame

(1)10ft/17ft Ext

(1)13ft/22ft Ext

Staging Units:  Units are pro-stage: metal frame ply top; need to be booked well in                                  advance

(6) 1000x2000x600

(6) 1000x2000x300

(6) 1000x2000x125

Stage Covers:   None

Stage Traps:     None

Safety Curtain:

Safety Curtain installed	NO

Loading Dock:

Access

Truck access via carpark off  High St. Truck able to reverse up to loading dock.(parallel)

Door Dimensions	3900 High

2950 Wide

Restrictions / Obstructions

Trucks must park parallel to loading dock. Loading dock is at stage level.

Additional Rigging Notes

There are no rated rigging points

Staging Notes:

All flown items must be rigged with rated equipment and is subject to approval by a venue representative

Access to the stage galleries is from the Bio box or Dimmer Room

Rigging gear is not available in house

LIGHTING

Positions:

Stage LX Bars	Fixed

See hanging plot for standard LX bar locations

Orchestra Bar

Pros Line to lighting bar	-300

Usable bar width	11000

Notes	Located underneath Catwalk

FOH Bridge #1

Pros Line to lighting bar	300

Usable bar width	8200

Notes                                       Refer to website

FOH Bridge #2

Pros Line to lighting bar	1900

Usable bar width	7300

Notes	Refer to website

FOH Bridge #3

Pros Line to lighting bar	4800

Usable bar width	3300

Notes	Refer to website

FOH Bridge #4

Pros Line to lighting bar	9300

Usable bar width	28600

Notes                                       Refer to website

Balcony Bar

Pros Line to lighting bar	14600

Usable bar width	7000

Notes	Refer to website

Control:

Lighting desk 	                  Strand 300 Series 48/96 Desk

Control channels	                    155

Signal output 	                  DMX 512

Signal distribution	Two streams of DMX. Stream A to dimmer room, stream B to various                                          points in gallery& around stage

Remote riggers available onstage	YES

Dimmer Racks:

Total dimmers @ 2.4kw per dimmer	108

Dimmer Locations	Dimmer room located on PS Gallery

3 phase outlets located in various positions around stage.

2.4Kw Dimmer Racks	(4)LSC LPak

(4)Bytecraft Solution 12

(1)LSC E Pak

House Lights:

Independant control	YES

Control positions	Control room & behind Pros Prompt side

Fade time adjustable	YES

Stage Luminare:

Profiles

| Make | Model | Angle | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- | --- |
| Strand | Pattern 23 |  |  | 650w | 6 |
| Selecon | Pacific | 23/50 | 8 IRIS,10 B Gobo holder | 600w | 28 |
| Selecon | Pacific | 14/35 | 10 A Gobo holder | 600w | 20 |

Fresnel’s

| Make | Model | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- |
| Strand |  | 6 barndoors | 1000w | 6 |

PC

| Make | Model | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- |
| Selecon | PC | 26 barndoors | 1200w | 26 |

Par Cans

| Make | Model | Angle | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- | --- |
| ETC | Source 4 |  | 4 lenses/ | 575 | 20 |

Wash

| Make | Model | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- |
| Selecon | Cyc Luminaire | (4) cells per unit | 500w | 10 |

Followspots:

| Make | Model | Angle | Detail / Accessories | Watt | Total |
| --- | --- | --- | --- | --- | --- |
| Canto | 700w MSR |  |  | 700w | 1 |

Power:

3 Phase Outlets

(10) in Dimmer room

(1) Op pros

(1) Prompt pros

(1) Rear wall stage OP

Cabling:

240v Extension Cable

The theatre has a good stock of extension leads to accommodate the venue’s standard lighting rig.

Looms

3 phase Extensions

(3) 20 Metre 32 Amp Wilco

Lighting Notes:

Lanterns for standard rig FOH can be relocated

On stage lighting bars cannot be swung

Access to orchestra bar from EWP positioned on stage floor

AUDIO

Control Positions:

Control Room

.

Auditorium

Rear centre of auditorium

Total seat allocation	5

Other

Almost anywhere backstage (extra patch loom may be needed in some positions)

.

Control & Amplification:

Primary Mixer

Allen & Heath GL 2400, 24 Channel, 2 stereo inputs, 4 aux sends, 4 groups, phtm power

Secondary Mixer

Allen & Heath 36+4ST:8:2:1 4eq 2 sweep HPF 8aux 4mute 2matrix

Amplifiers

(1) QSC PLX3002 2 X 900w @4Z (Subs: Hard-wired)

(3) QSC PLX2402 2 X 700w @4Z(FOH: Hard-wired)

(2) QSC PLX1602 2 X 500w @4Z (Foldback: Hard-wired)

(1)QSC PLX1202 2 X 325w @4Z (Rear auditorium Hard-wired)

EQ

(1) Klark Teknic

(2) LA Audio 231G

FX

(1)TC Electronics M ONE Digital effects processor

Compression / Limiter / Gates

(1)A & H IDR8 8x8 digital audio processor

(1) Klark Teknik Compressor

Speakers:

FOH Speakers

(6)Martin Audio15” 3way 400/150W bi-amp speaker (Fixed positions)

Foldback

(6)Martin Audio 12” 2way 300W speaker/wedge

Subs

(2)Martin Audio

Effect

(4) Martin Audio 2 X 5” ICT 50W 4/16Z (fixed)

Playback:

| Item | Make | Model | Detail | Total |
| --- | --- | --- | --- | --- |
| CD Player | Marantz | PMD340 | Single CD player | 1 |
| Minidisc/CD combo Player | Tascam | MDCD1 | SingleMD/CD | 1 |
| Cassette Deck | Marantz | PMD 502 | Single Tape | 1 |

Microphones:

| Make | Model | Detail / Accessories | Use | Total |
| --- | --- | --- | --- | --- |
| . Shure | SM58 | microphone clips | Vocals | 3 |
| RE | 510 Radio | microphone clips | Vocals | 2 |
| RE | 510 | microphone clips | Vocals | 4 |
| Shure | SM57 | microphone clips | Instrument | 4 |

Accessories:

| Item | Model | Detail / Accessories | Total |
| --- | --- | --- | --- |
| . Microphone stands | Tripod base | With boom arm | 10 |

Line Patching:

| Location | Quantity | Numbering | Detail |
| --- | --- | --- | --- |
| Catwalk | 12 | 1 - 12 | 12 sends |
| Pros Prompt | 8 | 13-20 | 8 sends |
| Rear Stage Wall Prompt | 8 | 21-28 | 8 sends |
| Rear Stage Wall Centre | 8 | 29-36 | 8 sends |
| Rear Stage Wall OP | 8 | 37-44 | 8 sends |
| Pros OP | 8 | 45-52 | 8 sends |
| DSC Trap | 8 | 53-60 | 8 sends |

Speaker Patching:

| Location | Quantity | Numbering | Detail |
| --- | --- | --- | --- |
| Various Catwalk | 4 | 1-4 |  |
| Adjacent to all line patching | 24 |  |  |

Cabling:

Audio Cable

The theatre has a good stock of cable to accommodate the venue’s equipment

Multicore: The theatre does not have a multi-core

Audio Notes:

FOH Speakers hard-wired

AUDIO VISUAL

Projectors:

| Type | Model | Detail / Accessories | Total |
| --- | --- | --- | --- |
| . Ben Q data projector | PB7200 | 1000 ansi, | 2 |

Screens:

Projection Screen

NO Screen   (Hired in or use Cyc)

.

Additional Screens

Hired in

AV Playback Equipment:

| Item | Model | Detail / Accessories | Total |
| --- | --- | --- | --- |
| Pioneer DVD | DV676A-S | Single DVD player | 1 |
| Philips DVD | DVP3020 | Single DVD player | 1 |

Projector Rigging Points:

Rigged from FOH LX Bars

Cabling:

The theatre has a reasonable stock of VGA & RCA cable to accommodate the venue’s own equipment

.

Audio Visual Notes:

Lack of depth on the stage area restricts rear projection options

BACKSTAGE

Communications:

Stage Managers Desk

Stage Managers desk is located in op corner. The desk can be moved within area this (or where ever ) and is fitted with a light, headsets, paging mic. & monitor

Talkback

Master Unit	ClearCom PL PRO MS 440 system running a common loop. The loop can carry up to 8 sub stations

Beltpacks	8

Total headsets	8

Radio Units In-house	Have to be hired in

Talkback patching located at:	Control Room (Master unit)

Stage Managers Desk

OP & P Stage

Various Positions Catwalk

FOH Bridge Followspots (2)

Production desk (auditorium)

Various positions Backstage

:

Paging / Show relay

Paging to the dressing rooms is available from the stage managers desk & bio box. Show relay is distributed to all dressing rooms and green room. Each room has an individual volume control

Stage Monitor

TV’s set-up in green room, foyer and SM position. Camera located centre of the Balcony Bar.

Dressing Rooms:

| Dressing Room | Capacity | Toilets | Shower | Details |
| --- | --- | --- | --- | --- |
| . Dressing Rm #1 | 4 | 1 | YES | Availability negotiated depending on |
| Dressing Rm #2 | 3 | 1 | YES | Hires in other theatres |
| Dressing Rm #3 | 3 | 1 | YES |  |
| Dressing Rm #4 | 5 | 1 | YES |  |
| Dressing Rm #5 | 3 | 1 | YES |  |
| Dressing Rm #6 | 3 | 1 | YES |  |

Laundry / Wardrobe:

Washing Machine		Yes

Dryer			Yes

Drying rooms		N/A

Iron / ironing board		Yes

Clothes racks		Plenty

Production Facilities:

Production Desk

Can be set up in centre of Auditorium. Seats 2, has DMX, Lighting board monitor & headset

Production Office

Production office available backstage in technical manager’s office.

Phone

Access to phone in Technical Management office

Fax

YES Available in Administration

Access to phone for internet access

Access to technical office phone line on arrangement with Technical Management.

Greenroom:

Tea / Coffee facilities	Yes

Fridge / freezer		Fridge

Microwave			Yes

Running water		Sink & washing up facilities

Stage Door:

Access

Stage Door is located beside the loading dock on High St. Access during bump-in / out will be controlled by the duty technician. During performance periods access is by arrangement.

ADDITIONAL FACILITIES & INFORMATION

Orchestral:

(2) KawaiI Grand piano. Relocation and tuning to be arranged prior to use

(60) Music Stands & black padded seats with backrest

(15) Sconce Lights

Rehearsal Space:

Rehearsal Room #1, 10m x 10m, timber floor, bookings required for use

Rehearsal Room #2 & #3, 12m x 6m, carpet on concrete floor, bookings required

VENUE:

Venue Contacts:

Venue Bookings:          Tina Madgic       02 47237622

Producer:                      James Fischer  02 47237605

Technical Manager:       Geoff Turner      02 47237608

Venue Address	597 High Street Penrith

Venue Postal Address	PO Box 2 Penrith 2750

Staff Contacts:

Box Office

Phone Number	02 47237600

Email Address	boxoffice@jspac.com.au

Fax Number	02 47313701

Venue Plans:

Venue Plan Available

Available on website

.

Venue Section Available

NO

Venue Information:

The Joan Sutherland Performing Arts Centre operates three performance spaces. The main venue is a Concert Hall with seating for 600 people. The second venue is The “Q”Theatre with seating for 375 people. The third venue is less formal with seating for 90 people

The venue is located adjacent to Penrith Plaza (which is huge). It has many take away outlets and two supermarkets within 50 mtrs of the theatre. Woolworths  are open between 8am and 9pm, all week